Configuration Files

The configuration file is a text file that contains a user’s options for a particular problem to be solved with the SU2 suite. It is specified as an input upon execution of SU2 components.
The SU2 configuration file name typically carries a name of the form filename.cfg. The file extension .cfg is optional (this is our own convention), and the prefix can be any valid string with no spaces; e.g. config.cfg, su2-config.cfg, and flow_config.cfg are all suitable file names.

The configuration file consists of only three elements:

- Options. An option in the file has the following syntax: option_name = value, where option_name is the name of the option and value is the desired option value. The value element may be a scalar data type, a list of data types, or a more complicated structure. The “=” sign must come immediately after the option_name element and is not optional. Lists of data types may be formatted for appearance using commas, ()-braces, {}-braces, and []-braces, though this is not required. Semicolons are semantically relevant for several option types and may not be used as convenience delimiters. SU2 will exit with an error if there are options in the config file which do not exist or if there are options with improper formatting.
- Comments. On a given line in the file, any text appearing after a % is considered a comment and is ignored by SU2. Additional % signs after the first on a given line are not significant.
- White space. Empty lines are ignored. On text lines that define options, white space (tabs, spaces) can be used to format the appearance of the file.

Mesh Files

SU2 mainly uses a native mesh file format as input into the various suite components. Limited support for the CGNS data format has also been included as an input mesh format. CGNS support can be useful when it is necessary to create complex geometries in a third-party mesh generation package that can export CGNS files. A converter from CGNS to the native format is also built into SU2.

### Description
The SU2 mesh format carries an extension of .su2, and the files are in a readable ASCII format. As an unstructured code, SU2 requires information about both the node locations as well as their connectivity. The connectivity description provides information about the types of elements (triangle, rectangle, tetrahedron, hexahedral, etc.) that make up the volumes in the mesh and also which nodes make up each of those elements. Lastly, the boundaries of the mesh, or markers, are given names, or tags, and their connectivity is specified in a similar manner as the interior nodes.
## CGNS Format

The native format is straightforward and readable, and meshes for simple or analytic geometries can be made very easily using scripts like those provided above. However, for creating meshes around very complex geometries, third party meshing software can make the process much simpler than attempting to build meshes via scripting. With this in mind, support for the CGNS data standard has been included within SU2. The main advantage gained here is that complex meshes created in a third party software package (one that supports unstructured CGNS file export) can be used directly within SU2. Furthermore, a converter from CGNS to the .su2 format has been built into SU2.

Abstract:
Interconnected systems with the parallel threading framework running in multiple cores between the shared systems and one core used for GUI performance which displays the performance of the real time application. The GUI also allows the probing for different analyisis' and displays the efficiency and performance of parallel computation and how the performance changes when we increase no.of nodes.
Experiment:	pc2
4 THREADS

Pc1 CROSSOVER SSH
GUI FOR METRICS / 4 THREADS

Two laptops are inter connected via crossover cable using SSH. Laptop contains 4 cores with 2 threads per core, so conceptually 8 CPUs work in both Laptops.one core will be used for running the GUI (made using Python3 the Tkinter Libraraies) which will display various metrics of the application say the parallel threads running,computational time,latency, and various metrics related to the application. Options present in the GUI will help in setting the priorities of the threads to observe the differences as well as see the share of CPU and Memory usage.
Goals of parallelisation:
1.Reduce the task assigned to each node
2.Reduce the computational time
3.Improve overall efficiency

Metrics in the GUI will be calculated using 'Dynamic Instrumentation.'

Learning:
     0. Two laptops with windows or linux os
1. GUI: Python3 and Tkinter
2. SU2 libraries
3. OpenMP
4. MPI
5. Use of SSH for communication.